## Slide 1: GPS-Based Road congestion detection
Ashwin Revo, Fei Xiang, Osman Sayli

## Slide 2: Congestion...

## Slide 3: Problem Statement
The aim of the project is to detect road congestion conditions using location information of vehicles on the road
The location of vehicles is obtained from the GPS devices on user mobile phones
The road congestion will be characterized as high, moderate and null

## Slide 4: Congestion detection problem
Location information of vehicles continuously relayed by GPS enabled cell phones
Speed of vehicles estimated using location information at multiple sampling instants
Using estimated speeds, traffic congestion detected
  H0 – No congestion
  H1 – Moderate congestion
  H2 – High congestion
H0 | Speed > γ2
H1 | γ1 <Speed < γ2
H2 | Speed < γ1

## Slide 5: GPS Error
Triangulation depends on:
(1) Satellite position (ephemeris error)
(2) Satellite clock (clock error)
(3) Time delay (time at which signal is received on Earth)
Other sources of error are Atmospheric error, Numerical error, Multipath etc.

## Slide 6: GPS Error
There is an error at every stage.
GPS Location fix:
Commercial GPS receivers can give a fix with an accuracy of ± 15m (typically accuracy)
PDOP – Position Dilution of Precision

## Slide 7: Algorithm Overview
Step 1: Position estimation
Step 2: Speed estimation
Step 3: Do speed estimation for multiple cars and multiple intervals within a certain block of road. Get a vector of speeds of different cars during different intervals.
Assumption: vector of speeds corresponding to 1mile belong to same hypothesis

## Slide 8: Algorithm Overview
Step 4: Create three hypothesis representing different levels of congestion. (This depends on which road the speed data are coming from.)
Step 5: Use Neyman-Pearson Test to find the thresholds.
Step 6: Use the LRT to detect which hypothesis is true.

## Slide 9: Estimation of Speed
is some non-random value.
Estimator is unbiased and efficient.
(P1 and P2 are the actual positions of car)

## Slide 10: Estimation of Speed
For vehicle i, the estimations of speed in different time intervals are:
Combine all the speed estimations for each vehicle into a single vector:
The vector above will be used to detect the congestion status of the road.

## Slide 11: Detection of Road Congestion
Congestion Modeling
Assumption: Under each hypothesis, speeds of vehicles on the road have Gaussian Distribution(3)(4).
  H2 : High Congestion ~
  H1 : Medium Congestion ~
  H0 : No Congestion ~

## Slide 12: Detection of Road Congestion
Likelihood Ratio Test:
Thresholds ηij are unknown. Need to determine the thresholds using Neyman-Pearson test.

## Slide 13: Detection of Road Congestion
H2
H1
H0
η21
η10

## Slide 14: Detection of Road Congestion
Neyman-Pearson Test:
For hypothesis H0 ,
Given PF , we can solve for η10

## Slide 15: Detection of Road Congestion
Neyman-Pearson Test:
For hypothesis H1 ,
Given PF , we can solve for η21

## Slide 16: Detection of Road Congestion
Now we have η10 and η21 , we can do the detection using the LRT below:

## Slide 17: Analytical ROC
σ1 – standard deviation of H1
σ2 – standard deviation of H2
µ1 – mean of H1
µ2 – mean of H2
n – number of samples

## Slide 18: Analytical ROC

## Slide 19: Analytical ROC

## Slide 20: Estimator Performance
For an unbiased estimator,
  mse(Â) = var(Â) =
  mse reduces as ∆T increases
As ∆T increases, speed estimate does not match instantaneous vehicle speeds
Number of speed samples available for traffic detection reduces

## Slide 21: Sampling Rate

## Slide 22: Sampling Rate
Sampling instant of 2 seconds optimum

## Slide 23: Simulation – US1 South
Car traveling with speed = 18 mph
Congestion - High
Car traveling with speed = 72 mph
Congestion - Null

## Slide 24: Conclusion
Developed an algorithm for road traffic detection
Based on speed estimation from GPS coordinates of on road vehicles
Calculation of system parameters studied
Algorithm results verified using simulations

## Slide 25: References
Mobile Millennium Project, http://traffic.berkeley.edu/index.html
http://en.wikipedia.org/wiki/Global_Positioning_System
Joonho Ko, Randall L. Guensler, ‘Characterization of Congestion Based on Speed Distribution: A Statistical Approach Using Gaussian Mixture Model’
Kloeden CN, Ponte G, McLean AJ, ‘Travelling Speed and the Risk of Crash Involvement on Rural Roads’